## Slide 1: The Biotic Ligand Model: Unresolved Scientific Issues and Site- and Species-specific Effects on Predicted Cu Toxicity
Jeffrey Morris,1 Ann Maest,1 Alison Craven,2 and Joshua Lipton1
1 Stratus Consulting Inc.
2 University of Colorado-Boulder
Boulder, CO
EPA Hardrock Mining Conference 2012: Advancing Solutions for a New Legacy
Denver, CO
April 4, 2012

## Slide 2: Background
The Biotic Ligand Model (BLM) is used to evaluate the site-specific toxicity of copper to aquatic organisms
  Can be used to develop site-specific water quality criteria (EPA, 2007)
  Ongoing investigations into different aspects of the Cu-BLM: geochemical, biological
Current research: quantifying Cu-organic carbon complexation in low hardness waters and subsequent implications for predicting fish toxicity using the BLM

## Slide 3: Presentation Outline
Overview of BLM
Site-specific Cu-binding studies and metal-DOM binding
Cu toxicity in low-hardness waters
Approaches to incorporating Cu binding constants of “biotic ligands” into BLM

## Slide 4: BLM: Background
Water quality criteria for Cu (and many other metals) expressed as a function of hardness.
  Increased hardness => decreased toxicity => higher WQC
    Observed in many controlled experiments
Well understood that Cu toxicity to aquatic biota is affected by other constituents in water
  Dissolved organic carbon has been found to reduce Cu toxicity
BLM developed to numerically address the influence of multiple chemical factors on Cu toxicity

## Slide 5: BLM: Conceptual Model
Cu speciation/sorption to gill binding sites (“biotic ligand”) affects bioavailability and toxicity
http://www.hydroqual.com/wr_blm.html
LBL

## Slide 6: BLM: Conceptual Model (cont.)
BLM: predict concentration of dissolved Cu that would cause toxicity to aquatic biota over a range of water quality conditions
  BLM uses “lethal accumulation” on gill to estimate toxicity
Three elements of model
  Geochemical speciation code CHESS (Santore and Driscoll, 1995)
    Calculates inorganic metal speciation
  WHAM V model (Tipping, 1994)
    Calculates degree of metal-organic interaction
  Biotic ligand (e.g., fish gill) binding constant (Di Toro et al., 2001)
Geochemical Speciation
Metal-organic Interactions
Binding to fish gill

## Slide 7: BLM Illustration: Acute WQC in the Presence of DOC

## Slide 8: Evaluating Cu-Organic Complexation in a Low-hardness Stream

## Slide 9: Site-specific Cu Binding Studies
Purpose: Evaluate Cu binding properties of ambient DOM
Performed laboratory studies of site-specific Cu binding in low-hardness waters
  Finding: Stream DOM had less ability to complex Cu than calculated by the BLM

## Slide 10: Methods
Isolated DOM from three low hardness headwater streams in AK
Cu-ISE titration
  Fit to a 2-ligand model
CLE-SPE (competitive ligand exchange-solid phase extraction)
  Environmentally relevant [Cu]
Used MINTEQ and empirically derived “effective log K” to estimate free Cu2+
Compared to BLM free Cu

## Slide 11: Ambient Water Quality
pH: 7.1–7.6
Alkalinity: 13.5–33.9 mg/L as CaCO3
Hardness: 13.4–28.4 mg/L as CaCO3
Dissolved Cu: 0.2–1.3 mg/L
DOC: 1.3–2.2 mg/L

## Slide 12: Results: Titration and CLE-SPE
“Effective log K” (net Cu complexation) of site waters a function of Cu:DOM ratio
Increasing Cu relative to ambient DOM results in lower log K

## Slide 13: Comparison with Other Studies
This Study

## Slide 14: Site-Specific Cu Binding Summary
Cu-organic binding a function of relative amounts of Cu and DOM present – net affinity changes as more Cu is added
  Distribution of binding sites in DOM
    High affinity (high log K) sites less abundant than lower affinity sites
    As Cu concentrations increase, progressive shift to binding with lower affinity sites
Cu:DOM ratio is important in predicting complexation

## Slide 15: Modeling Free Cu: Empirical Data

## Slide 16: Modeling Free Cu: Comparison to BLM

## Slide 17: Adjusting DOC Concentrations in BLM to “Match” Empirical Data
Previous authors (De Schamphelaere et al., 2004; Welsh et al., 2008) proposed adjusting DOC concentration (input to BLM) to match Cu-DOC complexation toxicity results
  Adjustment factor of 2 used
This study: adjust [DOC] from 2.2 mg/L to approx. 0.3 mg/L to match experimental data
  Adjustment factor of approximately 8
Notes: De Schamphelaere, K.A.C., Vasconcelos, F.M., Tack, F.M.G., Allen, H.E., Janssen, C.R., 2004. Effect of dissolved organic matter source on acute copper toxicity to Daphnia magna. Environ. Toxicol. Chem. 23, 1248–1255.
Welsh, P.G., Lipton, J., Mebane, C.A., Marr, J.C.A., 2008. Influence of flow-through and renewal exposures on the toxicity of copper to rainbow trout. Ecotoxicol. Environ. Saf. 69, 199–208.

## Slide 18: Adjusting DOC Concentrations

## Slide 19: Implications: Estimating Cu Toxicity with Adjusted DOC
~5-fold reduction in effects concentration

## Slide 20: Summary of Cu Binding Results
BLM under-predicted free Cu compared to site-specific estimates
Needed to lower DOC in BLM to attain same free Cu results – similar findings to other researchers (e.g., De Schamphelaere et al., 2004; Welsh et al., 2008), but somewhat greater magnitude of adjustment
Results in a ~ 5-fold decrease in instantaneous WQC compared to BLM

## Slide 21: Other Issues: Modeling Cu in Low Hardness Waters?
Ran series of BLM simulations to further evaluate implications of Cu-DOC complexation in low hardness waters
Used site-water data as base water quality
  Temperature = 19°C
  pH = 7.13
  DOC = 2.17 mg/L (HA = 10%)
  Ca, Mg = 4.09, 1.1 mg/L (hardness = 14.7 mg/L CaCO3)
  K = 0.1 mg/L
  SO4 = 1.7 mg/L
  Cl = 0.5 mg/L
  Alkalinity = 22.3 mg/L CaCO3
  S = 0.001 mg/L (default, non-functional)

## Slide 22: Simulation Results: Varying Hardness; Unadjusted DOC

## Slide 23: Simulation Results: Rainbow Trout LC50 Varying Hardness and DOC

## Slide 24: Hardness Simulation: Artifact of DOC Complexation?

## Slide 25: Equivalent LC50, 10-fold Difference in Hardness

## Slide 26: BLM Simulations: Summary
Outputs at low hardness in BLM suggests Cu preferentially bound to DOC rather than the biotic ligand (gill)
BLM may under-predict toxicity of Cu because of DOC complexation (log K data)
Degree of under-predicted toxicity of Cu may be exacerbated in soft water

## Slide 27: Predicting Cu Toxicity: Implications of Biotic Ligand Component
Cu toxicity a function of relative complexation: log K of DOC v. log K of biotic ligand
Biotic ligand not as refined as other two BLM components
Current BLM uses a constant log K value for the biotic ligand
  Shifts in relative log K of DOC in water v. constant log K in biotic ligand alter predicted toxicity

## Slide 28: Biotic Ligand (gill) Log K in the BLM

## Slide 29: Log K in the BLM

## Slide 30: Shifts in Apparent Gill Log K with Hardness?
Bielmyer et al., 2008.

## Slide 31: Measured Gill Log Ks in Different Species

## Slide 32: Effects of Varying Log K on Predicted Toxicity

## Slide 33: Biotic Ligand Log K Summary
Gill Log K known to change with water chemistry – dynamic
Using Log Ks developed for different species may result in ~ 2-fold change in LC50 at DOC = 2 mg/L
Variable log K in gill + variable log K in site water = variable predicted toxicity

## Slide 34: Conclusions
BLM under-predicted free Cu compared to site-specific estimates
Needed to lower DOC in BLM to attain same free Cu results – similar findings to other researchers (e.g., De Schamphelaere et al., 2004; Welsh et al., 2008), but somewhat greater magnitude of adjustment
  ~ 5-fold decrease in instantaneous WQC

## Slide 35: Conclusions (cont.)
Simulation modeling with BLM suggests Cu preferentially bound to DOC rather than the biotic ligand (gill) at low hardness
Degree of under-predicted Cu toxicity
Variable log K in gill + variable log K in site water = variable predicted toxicity
Uncertainty in Cu toxicity can be reduced with supplemental site-specific data
  Cu-DOC complexation
  Species-specific toxicity testing